## Slide 1: A Hand-held Device Software Development Project
Goal: build a hand-held device software.
Example products: detection probe for surface temperature, device movement speed, motor control, etc …
Objectives:
Start with feasibility study with specifications and requirements, resources and tools.
Assist in hardware design, test, deploy, and sustain the software.
Perform failure mode evaluation and analysis.
Documentation and training.

## Slide 2: A Hand-held Device Software Development Project
Sensors input –
Indication Outputs –
Accessory –
On-board MCU
System Main Controller
(not part of the device)
Arrows: by-directional serial communication links for command and data carried by message protocol
Hand-held Device

## Slide 3: Hand held Device
Sensors input –
External temperature
Optical for XY and speed
Indication Output –
Audio
LED array
One-time-use part –
Control, detection, and management
on-board MCU
State machine, on-chip and external peripheral I/O management.
Host communication protocol and management for request and response.
Self-diagnostics, firmware download, etc …
System Main Controller
Master control the hand-held device and process data collected from hand-held device

## Slide 4: System Requirement and Specification
Speed and robustness
Peripheral specification from data sheet
Hardware resource
Maintenance and upgrade
Software development tool and resource
Failure exception detection and recovery

## Slide 5: Firmware Design
Distributed computing
Inter-task communication and synchronization
Shared data buffer and concurrency control
Data access redundancy
Keep interrupt short and don’t use blocking call in it.
Reduce use of global variables
Make use of volatile modifier
Don’t do long or big computation in interrupts

## Slide 6: Firmware Design (continue 1)
MCU software model and deployment
non-OS driven and use IAR System tool to build
Use J-tag interface command line utility to download application Firmware to the on-board flash memory
Peripheral I/O configuration, control, communication, and UI model
SPI, I2C, RS232, PWM, A/D, D/A. programmable counter array, etc …
Protocol for command and data exchange with the host
Communication and bus speed
Provide audible and visible indication for normal operation and failure status

## Slide 7: Firmware Design (continue 2)
State machine model
Divide SoC Timer to partitions to allocate use of MCU
Each time-partition supports one or more peripheral
Combined time-partition management with peripheral interrupts
Peripheral interrupt priority management
Back-ground and house keeping tasks
Test and Debug
Have some GPIO I/O pins to facilitate test/debug
Use protocol analyzer and scope to measure timing